All construction, remodeling and development projects have the potential to create negative impacts to local water quality.  If you have a small project that creates or replaces less than 2,500 square feet of impervious surface, please consider implementing the appropriate site design measures and pollution prevention source control measures relevant to your project that are listed below.  Your project is also required to implement relevant construction activity Best Management Practices (BMPs), based on the BMPs Standards listed below, in order to prevent sediment or other pollutant discharges to the City’s storm water drainage system.

Consider Selecting Appropriate Site Design Measures to Prevent Stormwater Runoff Pollution

Site Design measures are project features that reduce water quality impacts by reducing impervious surface area and/or directing runoff from impervious surfaces to vegetated areas rather than directly to the street or storm drain system.

- Small projects that create or replace less than 2,500 square feet of impervious surface are encouraged to implement one or more site design measure, such as those listed below.

| Yes | No |  |  |
| --- | --- | --- | --- |
|  |  |  | a. Direct roof runoff into cisterns or rain barrels and use rainwater for irrigation or other non-potable use. |
|  |  |  | b. Direct roof runoff onto vegetated areas. |
|  |  |  | c. Direct runoff from sidewalks, walkways, and/or patios onto vegetated areas. |
|  |  |  | d. Direct runoff from driveways and/or uncovered parking lots onto vegetated areas. |
|  |  |  | e. Construct sidewalks, walkways, and/or patios with permeable surfaces. |
|  |  |  | f. Construct driveways and/or uncovered parking areas with permeable surfaces. |
|  |  |  | g. Minimize land disturbance and impervious surface (especially parking lots). |
|  |  |  | h. Maximize permeability by clustering impervious areas and preserving open space. |
|  |  |  | i. Use landscape-based stormwater retention features. |
|  |  |  | j. Protect sensitive areas, including wetland and riparian areas, and minimize changes to the natural topography. |

Consider Selecting Appropriate Source Control Measures to Prevent Stormwater Runoff Pollution

Source Control measures are project features that prevent potential pollutant sources from ever contacting rainfall or stormwater runoff.

- Small projects that create or replace less than 2,500 square feet of impervious surface are encouraged to implement one or more appropriate source control  measures, such as those listed below.

| Yes | No |  |  |
| --- | --- | --- | --- |
|  |  |  | a. Covering trash, food waste, recycling and compactor enclosures |
|  |  |  | b. Installing appropriate covers, sanitary sewer drains and storage precautions for outdoor material storage areas, outdoor work and/or wash areas, repair and maintenance areas and fueling areas. |
|  |  |  | c. Landscaping that minimizes irrigation and runoff, promotes surface infiltration where possible, minimizes the use of pesticides and fertilizers, and incorporates appropriate sustainable landscaping practices and programs such as By-Friendly Landscaping. |
|  |  |  | d. Stenciling/marking storm drains with messages such as “No Dumping, Drains to Bay” or “Only Rain Down the Storm Drain” |
|  |  |  | e. Plumbing of swimming pool, fountain or spa drainages to the sanitary sewer if discharge to onsite vegetated areas is not a feasible option. |
|  |  |  | f. Plumbing the discharges of any outdoor wash areas for vehicles, equipment or accessories to the sanitary sewer. |
|  |  |  | g. Plumbing the discharges of dumpster drips from covered trash, recycling and green waste enclosures to the sanitary sewer. |
|  |  |  | h. Plumbing the discharges of fire sprinkler test waters to the sanitary sewer sytem if the discharge to onsite vegetated areas is not a feasible option. |

Implement Construction Best Management Practices (BMPs) (Applies to all projects)

|  | All construction projects, regardless of size, are required to effectively implement appropriate stormwater best management practices (BMPs) to protect water quality discharges to the stormwater drainage system. Projects shall implement relevant BMPs to prevent the discharge of any and all potential pollutants, including, but not limited to, debris, trash, pavement cutting wastes, paints, concrete, petroleum products, chemicals, sediment, or any wash or rinse water to the stormwater drainage system or any waterway. |
| --- | --- |

| Yes | No | Check that your project is implementing all relevant Best Management Practices (BMPs) |
| --- | --- | --- |
|  |  | Require your contractor to implement BMPs to keep a clean site and prevent runoff pollution. |
|  |  | Gather and store all construction debris daily in appropriate containers which are emptied or removed on an at- least weekly basis. Prevent trash and litter accumulation on the ground. When appropriate, use tarps on the ground to collect fallen debris or splatters that could contribute to stormwater pollution. |
|  |  | Use a broom or other dry cleanup method to remove all dirt/mud, gravel, debris, refuse and green waste from all paved surfaces and the public sidewalk and street pavement on a DAILY basis and prior to rain. |
|  |  | Clean up leaks, drips and spills immediately. |
|  |  | Cover all temporary stockpiles securely with a tarp, plastic sheeting or similar material to prevent windblown dispersal or runoff of any material. |
|  |  | Use/create a contained and covered area on the site for the storage of cement bags, paints, flammables, oils, fertilizers, pesticides, or any other materials used on the project site that have the potential for being discharged to the storm drain system by wind, exposure to rainfall or in the event of a material spill. |
|  |  | Provide erosion “prevention” (soil stabilization) and site perimeter protection measures such as fiber rolls, silt fence, and/or sediment traps or basins to prevent any sediment from leaving the work site. Maintain these measures to remain effective. |
|  |  | Install and maintain a stabilized construction entrance to minimize the tracking of dirt, mud, dust and/or debris onto the public right-of-way. During wet weather, avoid driving vehicles where mud or other wastes can be tracked onto the public right-of-way. |
|  |  | Protect all storm drain inlets in the vicinity of the work site using filter materials such as gravel bags and filter fabric. Inlet protections shall be installed prior to any activity that may result in the discharge of material to the storm drain. Maintain these filter materials to remain effective and remove any accumulated sediment deposits. Remove these materials during project wrap-up. |
|  |  | Divert on-site stormwater flows around areas of exposed or disturbed soil to prevent erosion or sediment runoff. |
|  |  | Design any site de-watering (i.e., the removal of water from an excavation pit) efforts to prevent the discharge of any sediment, debris or other pollutants to the street, sidewalk or stormwater drainage system. |
|  |  | Vacuum all pavement saw-cutting slurry immediately and remove from site. Do not allow pavement saw-cut slurry to accumulate or linger on the pavement or to enter the gutter or the downstream stormwater drainage system. |
|  |  | Avoid cleaning or rinsing any machinery, tools, brushes, equipment, containers, surfaces, etc. into a street, gutter, storm drain or waterway. |
|  |  | Ensure that concrete supply trucks and/or concrete/plaster operations do not discharge wash water or wastes into the street, gutters or stormdrains. Concrete trucks and mixing and/or pumping operations shall prevent splatter and spills directly onto the ground or paved surfaces and shall have a self-contained wash-out system or discharge to a dedicated, secure on-site wash-out. |
|  |  | Prevent the discharge of any treatment or rinse waters from surface finishing efforts for architectural copper, cement, plaster, etc., to the stormwater drainage system or any waterway. |

# Text boxes

Stormwater Pollution Prevention Checklist

for Small Construction, Remodeling and Development Projects Creating

Less than 2,500 square feet of impervious surface  (<2,500 sq ft)

City of Alameda
Public Works Department
950 West Mall Square, Room 110 
Alameda, CA  94501-7558

Phone: 510-747-7930 / Fax: 510-769-6030

- Using Project Site Design and Pollution Source Control Measures to Prevent Stormwater Runoff Pollution

II.  Implementing Construction Activity Best Management Practices